## Slide 1: Impromptu
B09901008 電機三 蕭千玓
https://github.com/Hsiao-Chien-Ti/Impromptu

## Slide 2: Introduction 01.

## Slide 3: What is Impromptu(即興曲)?
隨處可彈的鋼琴手套
手勢偵測切換音高(可關閉功能)
WiFi連接手機
APP控制
支援錄音功能
樂譜功能

## Slide 4: Motivation 02.

## Slide 5: Just for fun! APP store Piano sucks! Why Impromptu? Idea is everywhere! Be quiet and noisy!
無聊就想動動手指
手指太粗好難按
靈感稍縱即逝趕快錄下來
戴上耳機怎麼彈都不吵到別人

## Slide 6: Methods 03.

## Slide 7: Design
Pitch Switching
Fingertips
WiFi
APP

## Slide 8: Components
STM32-L4S5I
Keyes薄膜壓力感測器
迷你麵包板

## Slide 9: Circuit Design

## Slide 10: Socket Programming
Server: Cellphone
Client: STM32

## Slide 11: Finger Tip Press
Keyes薄膜壓力感測器
AnalogIn read_u16()
Threshold: 14000
和threshold比大小後傳送0/1給server

## Slide 12: Pitch Switching
STM32加速度感測器
DSP FIR lowpass filter
Threshold:-30, 30
+
+
-
-
音高++
音高--

## Slide 13: APP
Android Studio Kotlin
4 Fragments: Navigation
SocketHandler, SettingVariable: Object, Thread, Volatile
Socket Programming: ServerSocket
播放音樂：SoundPool
錄音功能：MediaRecorder (需要權限)
範例樂譜：RecyclerView
設定：Switch component

## Slide 15: Demo Video 04.

## Slide 17: References 05.

## Slide 18: REFERENCES
1. Android studio: https://developer.android.com/courses/android-basics-kotlin/course?authuser=3
2. MbedOS: hw2, hw7
3. Previous work: https://www.amazon.com/Electric-Piano-Gloves-Playable-Interactive/dp/B00PTMORKS